## Slide 1: Characterizing and Modeling the Impact of Wireless Signal Strength on Smartphone Battery Drain
Ning Ding
Xiaomeng Chen
Abhinav Pathak
Y. Charlie Hu
Daniel Wagner
Andrew Rice

## Slide 2: Mobile Networks Connect the World

## Slide 3: Signal Strength Affects User Experience
Ideally
Reality…

## Slide 4: Complaints about Poor Signal

## Slide 5: Key Questions about the Impact of Signal Strength
How often are users experiencing poor signal?
How much is the impact on battery drain?
How do we model the extra energy drain?

## Slide 6: Key Questions about the Impact of Signal Strength
How often are users experiencing poor signal?
How much is the impact on battery drain?
How do we model the extra energy drain?

## Slide 7: Signal Strength Trace Collection
You transfer 3.7MB per day with WiFi, and 1.5MB per day with 3G
Your phone changes network cell 213 times per day
62% of your phone calls are less than 30s
Your average charging time is 42min
If the user permits, the app will upload anonymous
signal strength and location data

## Slide 8: Data Contributors
Traces (> 1 month) from 3785 users,
145 countries, 896 mobile operators
Contributors:
■ 1-10
■ 11-100
■ 101-1000

## Slide 9: Distribution of Wireless Technologies
100 sampled devices
WiFi 40%
HSPA 42%
UMTS 8%
None 8%
EDGE 2%

## Slide 10: Distribution of Wireless Technologies
WiFi and 3G (HSPA, UMTS) are the dominant wireless technologies

## Slide 11: 3G Signal Strength Distribution
Full bar
≥ -89dBm
Empty bar
≤ -109dBm
On average users saw poor 3G signal 47% of the time
Poor signal
≤ -91.7dBm [defined by Ofcom]

## Slide 12: Data Transferred under 3G
43% of 3G data are transferred at poor signal

## Slide 13: WiFi Signal Strength Distribution
Full bar
≥ -55dBm
Empty bar
≤ -100dBm
Poor signal
≤ -80dBm
On average users saw poor WiFi signal 23% of the time

## Slide 14: Data Transferred under WiFi
21% of WiFi data are transferred at poor signal

## Slide 15: Possible Reasons for Signal Strength Variations
A user with good 3G signal

## Slide 16: Possible Reasons for Signal Strength Variations
A user with medium 3G signal
A user with poor 3G signal

## Slide 17: Summary of Signal Strength Distribution
Users spend significant amount of time in poor signal strength
  47% of time in 3G
  23% of time in WiFi
A large fraction of data are transferred under poor signal strength
  43% of data in 3G
  21% of data in WiFi

## Slide 18: Key Questions about the Impact of Signal Strength
How often are users experiencing poor signal?
How much is the impact on battery drain?
How do we model the extra energy drain?

## Slide 19: Smartphones Used in Experiments
HTC Nexus One
802.11b/g
T-Mobile 3G
Motorola Atrix 4G
802.11b/g
AT&T 3G
Sony Xperia S
802.11b/g
AT&T 3G
Results shown are for Nexus One phone

## Slide 20: WiFi Experiment Setup
Laptop1: monitor mode, captures all MAC frames
Phone: performs 100KB socket downloading
Local server: runs socket server, emulates RTT using tc
Control signal strength by adjusting the distance
Laptop2: monitor mode, captures all MAC frames
Wireless router: connects to server with 100Mbps LAN
Powermeter

## Slide 21: WiFi Experiment Results
Flow time and energy for 100KB download with 30ms server RTT
-90dBm: 13x longer flow time, 8x more energy, compared to -50dBm

## Slide 22: WiFi Energy Breakdown Methodology
Power profile from powermeter
Packet traces from laptops
A snapshot of synchronized power profile and packet trace
Packet send
Packet recv

## Slide 23: WiFi Energy Breakdown
Energy breakdown

## Slide 24: WiFi Energy Breakdown Analysis
Retransmission rate
Data rate
Leads to higher Rx energy
Leads to higher reRx and idle energy

## Slide 25: 3G Experiment Setup
Local server: runs socket server, emulates RTT using tc, run TCPDump to capture packets
Phone: performs 100KB socket downloading, run TCPDump to capture packets
Control signal strength by changing location of the phone
Powermeter

## Slide 26: 3G Experiment Results
Flow time and energy for 100KB download with 30ms server RTT
-105dBm: 52% more energy, compared to -85dBm

## Slide 27: 3G Energy Breakdown Methodology
T-Mobile 3G state machine

## Slide 28: 3G Energy Breakdown
Energy breakdown
-105dBm: 184% more energy on Transfer, 76% more energy on Tail1, compared to -85dBm

## Slide 29: Key Questions about the Impact of Signal Strength
How often are users experiencing poor signal?
How much is the impact on battery drain?
How do we model the extra energy drain?

## Slide 30: Smartphone Energy Study Requires Power Models
Powermeter
Not convenient to use
Cannot do energy accounting
Smartphone
Power Output

## Slide 31: Train Power Models
Triggers
Power Model
Correlation between the triggers and energy consumption

## Slide 32: Use Power Models
Power Model
Triggers
Predicted power
Eliminates the need for powermeter
Enables energy accounting

## Slide 33: Three Generations of Smartphone Network Power Models
Power Model | Trigger | Network states | Subroutine-level energy accounting | Overhead
Low
Low
High
Utilization-based
Packet-driven
Bytes sent/received
System-call
driven
Packets
System calls
Incorporate the impact of signal strength

## Slide 34: Refine WiFi Packet-driven Power Model
WiFi power state machine
under good signal strength
Refine the model by deriving state machine parameters under different WiFi signal strength

## Slide 35: Refine 3G Packet-driven Power Model
3G power state machine
under good signal strength
Refine the model by deriving state machine parameters under different 3G signal strength

## Slide 36: Refine System-call-driven Power Models
Incorporate impact of signal strength on
  State machine parameters
  Effective transfer rate
Details are in the paper

## Slide 37: Evaluation of New System-call-driven Power Models
Model accuracy under WiFi poor signal (below -80dbm)
61.0%
5.4%
52.1%
7.2%
Model accuracy under 3G poor signal (below -95dbm)

## Slide 38: Conclusion
The first large scale measurement study of WiFi and 3G signal strength
  Time under poor signal: 47% for 3G, 23% for WiFi
  Data under poor signal: 43% for 3G, 21% for WiFi
Controlled experiments to quantify the energy impact of signal strength
  WiFi: 8x more energy under poor signal (-90dBm)
  3G: 52% more energy under poor signal (-105dBm)
Refined power models that improve the accuracy under poor signal strength
  WiFi: reduce error rate from up to 61.0% to up to 5.4%
  3G: reduce error rate decreases from up to 52.1% to up to 7.2%